## Slide 1
Design of a 16-Kb 1T1C DRAM for Conventional and Compute-in-Memory Access Modes Support
Hyeonjun Cheon, Jiwon Lee, Ho-Sung Lee, Ik-Hyeon Jeon and Joo-Hyung Chae
Department of Electronics and Communications Engineering, Kwangwoon University
Introduction
To realize high-performance AI, it is essential to move large amounts of data between memory and processing units.
By using the conventional memory access mode, chip performance is limited because limited data is read in one read operation.
To solve the bottleneck of data movement Compute-in-Memory(CIM) access mode is required.
By using CIM access mode, we could achieve 8 times faster operation speed than the conventional mode.
Also, our design shows 26.07% power reduction by using CIM access mode.
Therefore, if stability is ensured, CIM access mode can be good candidate to solve the bottleneck of data movement in AI semiconductor such as HBM-PIM.
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Overall Architecture
Measurement Results
Conclusion & Acknowledgement
Process | 28 nm CMOS
Memory type | DRAM
Array size | 16Kb
Maximum operation clock | Conventional: 150MHz, CIM mode: 200MHz
Supply voltage | 0.6V ~ 1.2 V
Average power | Conventional: 309.8 uW (150MHz, 1.2V) CIM mode: 229.03 uW (150MHz, 1.2V)
< Performance summary >
FPGA board is used to control the control logic signal for each command.
Our design could get a better shmoo plot for CIM access mode by reducing read cycles rather than conventional access mode.
< Measurement environment>
<Shmoo plot, L: conventional access, R: CIM access>
<Conventional memory access>
<Compute-in-Memory access>
The digital macro consists of a command control circuit.
It receives command signals from the FPGA and generates
control signals through the internally implemented finite
state machine (FSM).
An analog macro consists of a cell array and peripheral circuits
required for DRAM operation. It receives the FSM signal and
performs read and write operations.
The conventional memory access mode decodes 11bits of
ADDR and inputs and outputs 8bits of data.
The CIM access mode decodes 8bits of ADDR and inputs
and outputs 64 bits of data.
<Overall architecture of 16-Kb 1T1C DRAM>