## Slide 1
PAM-3 is being adopted as a standard in the recent memory interfaces to cope high-bandwidth, achieving higher BW than NRZ and better SNR than PAM-4.
Theoretically, PAM-3 achieves a 150% data rate improvement, but in memory interface, PAM-3 can not accurately make the burst length, there is only a 133% increase due to the dummy bit: e.g. BL 8 case.
The proposed scheme, by removing the DBI pin, can effectively achieve maximum pin efficiency and a 20.7% reduction in signaling power consumption.
Introduction
Proposed Scheme: Embedded pDBI for PAM-3
Implementation
Our design operates in NRZ and PAM3 modes for compatibility with previous generation memory.
NRZ/PAM-3 ZQ calibration saves the area of the comparator and digital logic through single loop.
Measurement
In pDBI encoding process, check the first 6bit/4UI and inverse the data according to whether the number of “1”s is more or less than 3.
The measured eye diagrams a 14 Gb/s at NRZ mode and a 25.2 Gb/s at PAM-3 mode.
The measured PAM-3 output level achieves the RLM of 98.5% through single loop ZQ calibration.
Compared to the previous design, the pDBI scheme achieves the best DBI efficiency of 19.3%.
Conclusion and Acknowledgement
The prototype chip of the NRZ/PAM-3 dual-mode TX was fabricated using a 65nm CMOS process.
By removing the DBI pin, it can achieve I/O bandwidth/pin efficiency of 133%.
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
A 25.2-Gb/s/pin NRZ/PAM-3 Dual-Mode Transmitter with Embedded Partial DBI Achieving a 133% I/O Bandwidth/Pin Efficiency and 19.3% DBI Efficiency
Chanheum Han*, Ki-Soo Lee*, and Joo-Hyung Chae (*Equally-contibuted Authors)
Electronics and Communications Engineering, Kwangwoon University