## Slide 1
Design of CMOS based ultra-wide range temperature sensor for quantum computing system
Chanjung Park, Jiyoung Kim, Kunhee Cho
Kyungpook National University, Daegu, Korea
Motivation
Temp. sensor which can be used for wide range is needed
  Cryogenic region operation is needed for quantum computing (4K)
  ON chip temperature sensing technique is needed for fast response
Temp. sensor relaxation oscillator
  BJT device does not work at cryo. region
Operation
Simulation Results
Temperature to Current conversion
  Beta-multiplier based sensing element
  TC depends on and of R
Current to Frequency conversion
  Current controlled Ring oscillator
Freq. to Digital code conversion
  12-bit digital counter
Implemented in 65nm CMOS process
PTAT current is achieved with resistance TC -0.367Ω/°C
PTAT frequency is achieved over a wide range of -270°C to 30°C (4K to 300K)
  0.833KHz/°C
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.