## Slide 1
연구개발내용
Design of Power Efficient Inductor-First Buck-Boost Converter Using Three Power Switches
Mina Shin, Kunhee Cho
Kyungpook National University, Daegu, Korea
Motivation
Inductor-first Buck-Boost DC-DC Converter is utilized
  Battery-powered application is being developed
    It can handle wide input voltage ranges and provide stable output voltages
  High efficiency is required for battery applications
    In placing the inductor at the input, lower inductor losses by reducing the flow of inductor current
Operation
Buck Mode
  At phase 1, Q1,3 are ON
    Since VCFH is VOUT and VCFL is 0V, CFLY is charged
  At phase 2, Q2 are ON
    Since VCFH is 2VOUT and VCFL is VOUT, CFLY is charged
  Conversion Ratio : 1/(2-D)
Boost Mode
  At phase 1, Q1,2 are ON
    Since both VCFH and VCFL are VOUT, CFLY is discharged
  At phase 2, Q3 are ON
    Since both VCFH and VCFL are 0V, CFLY is discharged
  Conversion Ratio : 1/D
Simulation Results
Implemented in 180nm BCD process
Inductor-first Buck-Boost Converter is demonstrated
  The peak efficiency of 98.7%/98.7% for Buck/Boost
  Three power switches are used
References
[1] Y. M. Ju, et al., ISSCC, Feb. 2017, pp. 184-185. [2] M. W. Ko, et al., ISSCC, Feb. 2018, pp. 428.429.
[3] Y. A. Lin, et al., VLSI, Jun. 2019, pp. C174-C175. [4] J. B. Baek, et al., ISSCC, Feb. 2020, pp. 202-203.
[5] H. Shin, et al., VLSI, Jun. 2021, pp.1-2.
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.