## Slide 1
<Schematic of Receiver>
In this work, we proposed an RF-to-BB CR mixer employing the IM2 injection technique. The core of the passive mixer operates as double-balanced mixer and sub-harmonic mixer (DBM/SHM) in sub-GHz and 2.4 GHz, respectively. The IM2 injection technique improves linearity by generating the in-phase fundamental signal and out-of-phase third-order-intermodulation (IM3) signal, compared to the passive mixer output. The auxiliary path for the linearization is designed to consume ultra-low power by employing a newly proposed current-reuse-based differential IM2 generator, passive multiplier, and current-steering-based summing stage.
<Simulation Results>
A Sub-GHz/2.4 GHz Highly Selective Reconfigurable RF Front-End Employing a Linearized RF-to-BB Current-Reuse Mixer
Dong-Min Kim, Dong-Myeong Kim, Ignacio Llamas-Garro, Dong-Gu Im
Department of Electronic Engineering, Chonbuk National University
E-mail : askd5736@naver.com, dgim@jbnu.ac.kr
A huge number of internet-of-things (IoT) devices (approximately seventy billion devices) will be connected to the global computer network, and this will make several challenges on the integration of heterogeneous devices and protocols, especially on the interoperability. The wireless connectivity technology has become a core technology for IoT sensor nodes, and the same clearly applies to it. A fully integrated RF transceiver operating in the both sub-GHz and 2.4 GHz license-free Industrial, Scientific and Medical (ISM) bands is highly required for low-cost IoT connectivity solutions supporting multi-protocol. It is well known that the sub-GHz RF radio using less bandwidth is more suitable for a low power long-range wireless communication with low-throughput and better sensitivity and, on the other hand, the 2.4 GHz ISM band is a better fit for a high data rate application within a smaller communication coverage. Because the future IoT sensor node needs to choose an optimum wireless communication protocol and optimize its power consumption according to the required data rate and communication coverage, the reconfigurable RF transceiver supporting the both sub-GHz and 2.4 GHz ISM bands becomes the best solution in implementing interoperable wireless connectivity technologies with low cost.
<Photograph of Layout and PCB Board>
This is fabricated die and measurement board photograph of the proposed RF front-end. The die includes Reconfigurable Balun-LNA, Linearized RF-to-BB Current-Reuse Mixer, LO Generator, and Measurement Buffer, and the test board includes control bits for tuning.
<Measurement results and Conclusion>
This shows the measured IIP3, IIP2 of the proposed RF front-end. The IB and OOB IIP2 were +24.7 ~ +27.3 dBm and +57.5 ~ +61.3 dBm in sub-GHz band. At 2.4 GHz, the measured IB IIP2 was +25.6 dBm. In sub-GHz band from 200 MHz to 800 MHz, the measured IB and OOB IIP3 ranged from -18 dBm to -15.2 dBm and from -0.4 dBm to -2.6 dBm respectively. At 2.4 GHz operation mode, the IB IIP3 of -15 dBm was obtained. In the case of NF, it showed 4.4 ~ 5.7 dB in sub-GHz band and 5.3 dB at 2.4 GHz. This work proposed a highly selective reconfigurable RF front-end using a balun-LNA covering sub-GHz and 2.4 GHz and linearized RF-to-BB CR mixer, for short- and long-range wireless connectivity technologies. As a result, the proposed RF-to-BB CR mixer alleviates the loading effect for the balun-LNA while achieving better gain, NF, and linearity with low power consumption.
<Acknowledgement>
The chip fabrication and EDA tool were supported by the IC Design Education Center (IDEC), Korea.
The proposed receiver was designed using a 65-nm CMOS process, and showed the simulation results of the double - sideband noise fig-ure (NFDSB) and output-referred third – order inter-cept point (OIP3 = IIP3 + gain) of only RF–to–BB CR mixer depending on there is the proposed linearization technique or not.
When the linearization technique is applied to the mixer operated in sub-GHz band, the average OIP3 improvement is about 8 dB and 6 dB when the two-tone spacing is 2 MHz and 20 MHz, respectively. At 2.4 GHz, it shows an average OIP3 improvement of 4 dB regardless of the two-tone spacing.