## Slide 1
Body-Biased Voltage-Latched Sense Amplifier with Rise-Time Control Technique for SRAM
Introduction
Jaehwan Kim and Taehui Na
Department of Electronics Engineering, Incheon National University, Incheon 22012, South Korea
Preliminary
Advancing process technology has increased transistor threshold voltage (VTH) variations, causing offset voltage (VOS) issues that affect memory read yield. To address these challenges, Body-Biased VLSA (BB-VLSA) is introduced. BB-VLSA utilizes body biasing and controlled slow rise-time (TRISE) to dynamically adjust pMOS transistor VTH. This technique reduces VOS and enhances differential signal injection (DSI) efficiency.
Sensing operation
In BB-VLSA, the body-biasing technique adjusts the VTH of transistors by manipulating the voltage between the source and body (VSB). The VTH of the pMOS (|VTHP|) is modeled by under equation
The DSI effect stems from the timing difference in the off states of the pMOS access transistors (MP3 and MP4) during sensing. Extending the TRISE increases the DSI duration and enhances ΔVBL, thereby improving the sensitivity and accuracy of the sensing operation in VLSA.
Proposed circuit
BB-VLSA enhances the conventional VLSA by connecting the body terminals of MP1 and MP3 to the BLB and the body terminals of MP2 and MP4 to the BL. Based on the |VTHP| Equation, the body-biasing technique employed in BB-VLSA allows to adjust the VTH of the pMOS by controlling the VSB.
BB-VLSA offers two advantages over the conventional VLSA :
First, it enhances the difference in driving strength between MP1 and MP2. Assuming that VBL > VBLB, the relationship between the body voltages of MP1 (VB_MP1) and MP2 (VB_MP2) is VB_MP1 < VB_MP2. As a result, the VTH of MP1 (|VTHP1|) becomes lower than that of MP2 (|VTHP2|).
Second, it reinforces the DSI effect between MP3 and MP4. The BB-VLSA, with the BLB connected to the body terminal of MP3 and BL connected to the body terminal of MP4, exhibits |VTHP3| < |VTHP4|. When VBL = VDD and VBLB = VDD – ΔVBL, the off time of MP4 (when VSAE = VBLB – |VTHP4|) remains the same as that of VLSA, while the off time of MP3 (when VSAE = VBL – |VTHP3|) is delayed, resulting in an increased DSI time.
Consequently, the BB-VLSA achieves an increased sensing ΔVBL, compared to the conventional VLSA, thereby reducing σOS.
BB-VLSA
Simulation and test-chip measurment results
Conclusion
The BB-VLSA utilizes body biasing to decrease VOS and facilitates a slow TRISE control technique to amplify the DSI effect, thereby further decreasing the VOS and energy consumption. Based on the simulation results using the 28-nm technology model, when the target σOS is 5 mV, the BB-VLSA with TRISE showed an 8.0% reduction in area and a 17.6% reduction in average energy compared to the VLSA with TRISE. Additionally, it demonstrated a 53.2% reduction in area and a 62.0% reduction in average energy compared to the VLSA without TRISE. Based on 28-nm test chip measurement results, a comparison between BB-VLSA and VLSA with the same transistor size revealed that BB-VLSA exhibited a smaller σOS across all TRISE ranges compared to VLSA. Furthermore, increasing TRISE led to a reduction in σOS for both BB-VLSA and VLSA.
DSI effect
SRAM with BB-VLSA and simulated waveform
Conventional VLSA and CLSA
Simulation results comparing the σOS and energy of BB-VLSA and VLSA under varying TRISE values
Area and energy consumption Comparison of BB-VLSA and VLSA at target σOS with TRISE and w/o TRISE
Transient simulation results
The effect of the parasitic capacitance of the buffer connected to the output node of SA
The σOS measurement results of the test chip
Summary of the simulation result
Layout of BB-VLSA and VLSA