## Slide 1
A Personalized Keyword Spotting Processor with High
Accuracy for 35 Classes
Introduction
Conventional Keyword Spotting Processor
Chip Photo & Comparison Table
KWS Model & Overall Architecture
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Acknowledgement
Hyuk-Jin Lee, Donghwan-Kim, Gi-Woo Lee and SeongHwan Cho
The School of Electrical Engineering of KAIST, Daejeon, Korea
Contributions and Scope of the Work
Implemented with Samsung 28nm Technology(SS28-2301)
Overall Architecture and Timing Diagram
Measurement Set-up
Chip Photo
Personalized Training only the last layer
  To ensure high linearity and resolution in the analog front-end, significant area and power consumption are inevitable.
  The use of FFT for feature extraction demands considerable area and power.
  Neural networks demand substantial memory and computation.
Block diagram of Conventional Keyword Spotting Processor
Proposed Keyword Spotting Processor
  Maintain high accuracy by using a personalized KWS network.
  Replace the FFT-based feature extractor with convolution layers.
Block diagram of Proposed Keyword Spotting Processor
Achieving high accuracy with a small number of parameters
Personalized Training
Convolution layer based Feature Extractor
Reducing area and computational load
Over 94% accuracy with fewer than 9k parameters
Only 0.005mm2 of area overhead for FE
  16 4-bit MAC operators are used for both FE conv operations and NN conv operations.
  One 8-bit MAC operator is used for inference in fully connected layer operations.
Overall Architecture
Timing Diagram
  Training the last layer speeds up learning and achieves high accuracy with minimal data.
  Smaller input features in the last layer also reduce memory size.
Personalized Incremental Learning
  Incremental learning involves integrating new data while preserving knowledge learned from past experiences.
On-Chip SRAM | 13kB
Supply Voltage | 0.6V-0.8V
Frequency | 1MHz
Power | 3.1uW
 | 2020 ISSCC | 2020 JSSC | 2021 ISSCC | 2021 JSSC | 2022 ISSCC | This work
Process | 28nm | 65nm | 180nm | 65nm | 65nm | 28nm
# of keywords | 2 | 12 | 1 | 7 | 12 | 35
Power | 510nW | 10.6uW | 148nW | 11mW | 23uW | 3.1uW
Accuracy | 94.6% | 90.9% | 94% | 90.4% | 86% | 94%
Accent speech recognition | x | x | x | x | x | o
Comparison Table